## Slide 1: Deep Learning Methods for Lift Risk Assessment
Brennan Thomas
Advisor: Dr. Rashmi Jha

## Slide 2: Goals
Determine if deep learning is a viable solution to detect risk of back pain caused by lifting heavy objects
Develop a machine learning approach to detecting the level of risk

## Slide 3: Intellectual Merits
Traditional human activity recognition systems focus on recognition of easily separable activities – walking, running, jumping, sitting, etc.
There is little research on different classes of similar activities
Provide insight into capabilities of machine learning for this use case

## Slide 4: Broader Impacts
Workplace ergonomics is a very important field
  Unsafe workplaces can have lasting impact on quality of life
Determining the usefulness of machine learning for monitoring workplace safety
Provides a framework for safer work environments using unintrusive wearable sensor monitoring

## Slide 5: Design Specifications
Consists of three components
  Preprocessing
    Prepares training/testing data
  Lift Detection
    Detects if a lift is occurring given a segment of IMU data
  Lift Risk Classification
    Classifies the risk level of a lift in a segment of IMU data

## Slide 6: Data Specification
Data collected by National Institute of Occupational Safety and Health (NIOSH)
Ten subjects, six lift trials in each zone defined by the American Conference of Governmental Industrial Hygienists (ACGIH) Threshold Limit Values (TLV) for lifting
Additional non-lifting trials

## Slide 7: Design Specifications - Preprocessing
Data split using leave-one-subject-out cross-validation
Samples segmented using sliding window for detection using binary labeling
Entire sample used as input for classification
No further preprocessing

## Slide 8: Design Specifications – Detection Model
6 Residual Blocks
2 LSTM layers
Fully-connected layer
Sigmoid output

## Slide 9: Design Specifications – Classification Model
Similar to detection
Softmax output
  1 unit for each class

## Slide 10: Technologies
Code is written in Python
  Tensorflow used for model implementations
  Numpy and Pandas for data preprocessing
  Scikit Learn for metrics
Machine Learning models
  Both models are implementations of deep learning networks
  Long Short-Term Memory Networks (LSTM) and convolutional layers form the core of the networks
IMU Sensors provide training and testing data

## Slide 11: Milestones
Preprocessing – Oct 26th, 2020
  Python code for preparing data for model consumption
Lift Detection – Dec 1st, 2020
  Python implementation of a machine learning model capable of detecting if a lift is occurring in a segment of IMU data
Lift Classification – Jan 5th, 2021
  Python implementation of a machine learning model capable of classifying a lift’s risk level from a segment of IMU data
Refinement – Feb 28th, 2021
  Modifications to previous milestones based on possible improvements

## Slide 12: Results – Lift Classification
Balanced Accuracy (BAC): 89.5%
Slightly biased towards samples with more data
Very good at separating lift and non-lift

## Slide 13: Results – Lift Detection
BAC: 92.9%
Suffers from poor precision due to unbalanced dataset
  F1 Score: 0.835
Positive predictions have around 50% chance to be negative
  Must be caught by classification model
 | Predicted Negative | Predicted Positive
Actual Negative | 35791 | 3858
Actual Positive | 185 | 4027

## Slide 14: Results
Comparative tests show that deep learning is a valid strategy for lift risk detection
Proposed implementation outperforms baseline
 | SVM | DeepConvLSTM | Proposed
Classification (BAC) | 0.609 | 0.832 | 0.895
Detection (F-score) | 0.450 | 0.732 | 0.835

## Slide 15: Challenges
Lift detection dataset is imbalanced
  Lifting action happens significantly less often than other activities
  Mitigated with rebalancing and data augmentation
Limited computing power and long train times
  Limit complexity of models and plan ahead for testing

## Slide 16: Thanks!
thoma2bm@mail.uc.edu